## Slide 1: SmartScan - Hierarchical Test Compression for Pin-limited Low Power Designs
ECE 7502 Class Discussion
Arijit Banerjee
03/26/2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Paper Map
[1] Chakravadhanula, K.; Chickermane, V.; Pearl, D.; Garg, A.; Khurana, R.; Mukherjee, S.; Nagaraj, P., "SmartScan - Hierarchical test compression for pin-limited low power designs," Test Conference (ITC), 2013 IEEE International , vol., no., pp.1,9, 6-13 Sept. 2013
[2] Muthyala, S.S.; Touba, N.A., "Improving test compression by retaining non-pivot free variables in sequential linear decompressors," Test Conference (ITC), 2012 IEEE International , vol., no., pp.1,7, 5-8 Nov. 2012
[3] Muthyala, S.S.; Touba, N.A., "SOC test compression scheme using sequential linear decompressors with retained free variables," VLSI Test Symposium (VTS), 2013 IEEE 31st , vol., no., pp.1,6, April 29 2013-May 2 2013
[4] Wohl, P.; Waicukauski, J.A.; Neuveux, F.; Maston, G.A.; Achouri, N.; Colburn, J.E., "Two-level compression through selective reseeding," Test Conference (ITC), 2 013 IEEE International , vol., no., pp.1,10, 6-13 Sept. 2013
[5] Bhatia, S., "Low power compression architecture," VLSI Test Symposium (VTS), 2010 28th , vol., no., pp.183,187, 19-22 April 2010
[2][3] Test cube compression using non-pivot free and retained free variables
[4] Two level compression using selective reseeding
[1] SmartScan Architecture
[5] Low power compression architecture
Hardware Architecture
Low Power, Good Coverage
Test Cube Compression Theory and Hardware
Test Compression
High Volume Compression
Moderate Compression in Data Volume, Test Time and Good Coverage

## Slide 4: Outline
Boundary Scan Chain and Scan Compression Overview
Important design parameters and Metrics
Discussion of the paper
Results
Other concepts in papers [2-5]
Discussion questions

## Slide 5: Boundary Scan Chain and Scan Compression Overview
Chip testing requires two criteria for testing
  Controllability of inputs
  Observability of outputs
Chips are pin limited
  Test pins are also limited
Boundary Scan
  A simple way to control and observe inputs and outputs: e.g. Joint Test Action Group (JTAG IEEE 1149.1)
  Need a separate chain of flip flops
  Need some extra pins (five) to control the scan chain
Issues with Boundary Scan
  Slow design
  Lengthy scan chain requires high test data volume test time
JTAG IEEE 1149.1 diagram from a tutorial document from http://www.asset-intertech.com

## Slide 6: Boundary Scan Chain and Scan Compression Overview Cntd.
Basic design for testability (DFT) Flow allows scan insertion
  Full Scan
    Replace all the flip-flops in a design with scan flops
  Partial Scan
    Replace some of the flip-flops with scan flops
Issues
  Slow scan design
  Lengthy scan chain requires high test data volume test time for big chips
Scan Insertion
http://teal.gmu.edu/courses/ECE545/viewgraphs_F06/synopsys_codes/synopsys_545/dft/dft.pdf

## Slide 7: Boundary Scan Chain and Scan Compression Overview Cntd.
One solution as improvement
  Dividing the scan chain in parallel
Scan loading time reduced
No impact on test data volume
Making scan chin parallel
From a PPT of Janak H. Patel at University of Illinois at Urbana-Champaign

## Slide 8: Boundary Scan Chain and Scan Compression Overview Cntd.
Basic Scan Compression Hardware
  Scan In Interface
  Decompressor
  Balanced scan chains
  Compressor
  Scan Out Interface
A white paper from www.cadence.com

## Slide 9: Boundary Scan Chain and Scan Compression Overview Cntd.
Decompressors
  Generates many output from less number of inputs
  Can be combinatorial XOR based or sequential linear feedback shift register (LFSR) based
Some combinatorial decompressors
  Broadcast (single input goes to multiple scan channels)
  Spreader (XOR based)
A white paper from www.cadence.com

## Slide 10: Boundary Scan Chain and Scan Compression Overview Cntd.
X-masking
  A way to prevent the X’s in the scan chains from propagating to the compressor and tester
  Improves compression ratio
Need extra mask control bits to load from the tester
A white paper from www.cadence.com

## Slide 11: Boundary Scan Chain and Scan Compression Overview Cntd.
Combinatorial compressors are usually XOR based that compresses the scan output to lower number of data bits
Sequential compressors are usually multiple input signature register (MISR) based
A white paper from www.cadence.com

## Slide 12: Important Design Parameters and Metrics
Test Access Time (TAT): Time to test
Test Data Volume (TDV): Data volume used in ATE
Test Coverage: Against a fault model how many faults are covered
Test Compression Ratio: The ratio of number of internal scan chains to the number of scan in pins
Scan Bandwidth: Number of scan in pins
Test Access Mechanism (TAM): A way (architecture) to test chip
TAM Width: The number of serial Si and SO pins in TAM

## Slide 13: Modern Scan Compression Architecture Needs
Multiple cores in system on chip (SoC) are pin limited: requires lesser test access pins
A test access mechanism (TAM) architecture require to compress and distribute the test data efficiently
Need support for high compression ratio, better coverage with a low pin overhead
Less switching to prevent chip damage or have logic issues while scanning multiple cores

## Slide 14: Issues with Conventional TAM Architecture
Target compression ratio is the close approximation of compression
With increase in compression ratio the internal scan chains getting identical data due to data correlation increases
High correlation compromises test coverage
It lowers coverage when the scan bandwidth is low
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 15: Issues with Conventional TAM Architecture Cntd.
With lower number of scan in pins (scan bandwidth) the fault coverage is lower compare to the full scan case for traditional TAM compression architecture
At the cost of increasing scan bandwidth we can have higher coverage
Lower coverage
with low scan bandwidth
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 16: SmartScan as a Solution
Key idea is to serialize the compressed stream of test data and control bits into core level
Allow SoC flexibility to interconnect the core level TAMs to top level tester pins
This improves fault coverage with lower scan bandwidth
Less switching lower test power preventing IR drop and prevents chip damage

## Slide 17: SmartScan Overview
Shift registers to serialize and de-serialize the data
Overlapped serializer and de-serializer (SERDES) I/O operations
X-masking is also supported
Mainly XOR based (applicable to MISR based also) compression scheme
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 18: SmartScan (SS) Operation with 8 bit SERDES and 2 Bit Scan
SS controller generates SERDES clocks, internal scan and mask registers
SS controller differentiate between the scan and mask load state with the scan_enable and mask_load_enable signals
Scan and mask clocks are mutually exclusive
Update captures the parallel in data from de-serializer which remains constant for the next N cycles
This allows the content to be shifted in the internal scan chains in a skew-safe manner
Also no switching activity in the decompressor due to new data shifting in from de-serializer
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 19: SmartScan (SS) Serial and Parallel Interface
A multiplexor at the output of each deserializer bit whose select is controlled by the SmartScan_enable and SmartScan_parallel_access signals
When SmartScan_parallel_access is true, the parallel scan pin feeds the decompressor and when false the deserializer feeds the decompressor
This happens If SmartScan_enable is true; when false the SmartScan logic is made testable as part of the fullscan chains
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 20: SmartScan (SS) Test Pattern Generation
Test generation is performed using N-bit wide parallel scan interface bypassing the deserializer/ serializer registers
Compressed patterns are generated using the parallel interface (N-scanin / N-scanout), and then simply retargeted to a SmartScan serial interface (e.g. 1 scanin / 1 scanout or 2 scanin / 2 scanout)
Each scan cycle of the parallel interface is translated into a load/unload of the deserializer/serializer registers
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 21: Key Advantages of SmartScan Parallel Interface
Decouples the mainstream DFT verification and pattern generation process from the SmartScan hardware
Greatly reduces the data correlation improves coverage
Internal scan configuration is identical between the parallel and serial interfaces and hence the pattern quality is identical as long as the patterns can be retargeted
Debug and diagnostics are minimally impacted, as tools can continue to diagnose using the parallel interface by translating serial failed pattern into parallel patterns

## Slide 22: Verification Checks in the SmartScan Logic
Verify the switch to serial interface and deserializer is feeding the compressor
Initial circuit state must be identical between the serial and parallel interface
Serial mode must have a sensitized path between serial scan in (scan out) pin and the first bit of the deserializer or serializer
Clock generation to the registers
Functionality of deserializer and serializer
Map each parallel scan in or out pin to its corresponding deserializer or serializer

## Slide 23: Programming Mask and Clock Control Registers
Programmable X-Mask and On-product Clock Generation (OPCG) Registers
Loading is done using the deserializer
ATPG test pattern load these pattern through the parallel interface
The pattern conversion process transform the data to be loaded via deserializer
Mechanism activating different states like scan_load, mask_load, OPCG_load is transparent to the pattern conversion process
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 24: Test Time Impacts Using SmartScan
Overall scan shift time for a single test pattern is N times longer
  Shifting of internal scan chain requires a complete load and unload of the N-bit deserializer and serializer
Overhead can be reduced using faster clocks in deserializers and serializers
  Typically ATE supports 4-6 times faster frequency than scan clock frequency
SmartScan parallel interface helps to lower pattern count due to reduced data correlation

## Slide 25: Hierarchical Test of Embedded Cores
Independent controllability and observability through SmartScan (SS) registers possible in each core
Identical cores can share the same deserializer(s), but need separate serializers
Heterogeneous cores can be tested simultaneously
  The cores can have different launch capture clocking sequence as the OPCG registers are loaded independently
  Inefficiency issue with grouping of highly unbalanced scan lengths in a core
Wiring congestion is less due to lower pin count in routed SS controller pins
Single sterilized out put to tell which core is bad
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 26: Addressing Power Issue in scan Shifting in SoC
Instantaneous switching in scan operation causes power issues in SoC
Solution
  Limiting the number of cores testing simultaneously
However, in unwrapped SoC level inter-core test all the cores will shift simultaneously causing power issue
  SmartScan interleaving clocking in solves this issue
  10X reduction in peak power drawn
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 27: Re-configurability in SmartScan
Re-configurability is a key feature eliminating test time or hardware overhead in multi core SoC
  Hierarchical test scenario with three cores and limited 2 Si and So pins
  Each core has 8 Si and 8 So pins: total of 24 Si and 24 So
Supporting flexible inter-core logic testing (multiplexing logic not shown)
  Multiple test schedule for inter-core testing: two core or three core etc. at a time
  A total of 24 deserializer (serializer) bits are distributed over the 2 scanins (scanouts), resulting in two 12-bit deserializer and two 12-bit serializer registers
  For two cores we only need 16 bit in total of deserializer (serializer) bits
  Interleaved SmartScan saves peak power
  Additional test schedules needed for intra-core testing if only one core is tested at a time
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 28: Physical and Timing Considerations
Deserializer (serializer) flip flops can be considered as pipelines
  Can be clustered together and locate far away from the scan pins on the SoC boundary
  Sometimes they can be present in the I/O pad
Types of pipes possible
  Internal and embedded pipes present in XOR logic
    Pipes behave identically in serial and parallel mode
  The external pipes present multiple challenges to the pattern conversion process
  Type 1: external pipes are those on the serial scan pins, e.g. SI1 and SO1. If the design does not have real parallel scan pins, Type-1 external pipes are bypassed in the parallel mode of operation; in the serial mode they are on the path to/from the SmartScan registers.
  Type 2: SI/SO 2-5
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 29: Integration with IEEE 1149.1 and P1687
SmartScan can be directly controlled from ATE or using IEEE 1149.1 (JTAG) TAP controller by decoding the state of the TAP FSM
Require simple translation or mapping of the SmartScan port to JTAG compatibility
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 30: Integration with IEEE 1149.1 and P1687 Cntd.
The serializer and deserializer sin the SmartScan can be treated as IEEE P1687 (iJATAG) compatible test data instruments and can be integrated with other P1687 compatible hardware
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 31: Experimental Results
Commercial design using TAM width of 1 SI - 1 SO or 2 SI - 2SO were used
Generated Fullscan (bypass) mode, in conventional XOR compression mode and in SmartScan mode
Due to data correlation effects, both in conventional compression and SmartScan the coverage is expected to be less than the fullscan
SmartScan achieves more coverage than conventional compression and requires less fullscan top-off vectors
SmartScan is 3.5X more faster than the conventions compression architecture as it requires a few Fullscan top-off pattern
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 32: Experimental Results Cntd.
Comprehensive results show a maximum of 26X TDV, 99.1% TAT reduction with above 99.2% coverage in most of the cases
Chakravadhanula, K. et al, "SmartScan - Hierarchical test compression for pin-limited low power designs," ITC, 2013 Sept. 2013

## Slide 33: Other Scan Compression Techniques: Case Study
Test cube compression
  Based on linear decompressor
Any decompressor that consists of only wires, XOR gates, and flip-flops is a linear decompressor and has the property that its output space (the space of all possible vectors that it can generate) is a linear subspace spanned by a Boolean matrix
A linear decompressor can generate test vector Y if and only if there exists a solution to the system of linear equations AX = Y, where A is the characteristic matrix for the linear decompressor and X is a set of free variables shifted in from the tester (you can think of every bit on the tester as a free variable assigned as either 0 or 1)

## Slide 34: Other Scan Compression Techniques: Case Study
The characteristic matrix for a linear decompressor is obtainable from symbolic simulation of the linear decompressor; in this simulation a symbol represents each free variable from the tester
Encoding a test cube using a linear decompressor requires solving a system of linear equations consisting of one equation for each specified bit, to find the free variable assignments needed to generate the test cube
If no solution exists, then the test cube is unencodable

## Slide 35: Other Scan Compression Techniques: Case Study
[2] is about test compression by retaining non-pivot free variables in sequential linear decompressors
Can encodes multiple test cubes
[2]

## Slide 36: Other Scan Compression Techniques: Case Study
Proposed hardware in [2]
  Instead of loosing the tester data after each q cycles, it keeps it in a FIFO to reuse it for encoding
Maximum TDV reported is 26%
Maximum coverage not reported
[2]

## Slide 37: Other Scan Compression Techniques: Case Study
Proposed hardware in [2]
  Instead of loosing the tester data after each q cycles, it keeps it in a FIFO to reuse it for encoding
  Maximum TDV reported is 26%
  Coverage not reported
Proposed architecture in [3] is SoC level
  Maximum TAT and TDV reported is 54.80%
  Coverage not reported
Proposed hardware in [2]
Proposed architecture in [3]

## Slide 38: Other Scan Compression Techniques: Case Study
Proposed concept in [4] is selective reseeding
  Load care bits and X-control input data are encoded into PRPG seeds generation
  Next, seeds are selectively shared for further compression.
The latter exploits the hierarchical nature of large designs with tens or hundreds of PRPGs.
The system comprises a new architecture, which includes a simple instruction-decode unit, and new algorithms embedded into ATPG
Maximum TAT reduction 185X
Maximum TDV reduction 305X
Maximum reported coverage 95.58%
Proposed hardware in [2]
Proposed architecture in [4]

## Slide 39: Other Scan Compression Techniques: Case Study
Proposed concept in [5] is a low power scan compression scheme
  Modified the Illinois- scan also known as Broadcast scan chain based DFT compression
  Shifting the scan chains one at a time using a one hot counter
Maximum TDV reduction 8X
Maximum reported coverage 99.2%
Maximum power reduction 2X
Proposed architecture in [5]

## Slide 40: Comparison of Test Design Metrics Across The Papers
Comparison of Test Design Metrics (Test Coverage, Test Access Time, Test Data Volume) for various Papers Related to Test Compression
Design Metrics | [Wohl et. al 2013] | [Chakravadhanula et. al 2013] | [Muthayala 2013] | [Muthayala 2012] | [Bhatia 2010]
Maximum Reported coverage | 95.58% | 99.91% | - | - | 99.2
Maximum Reported TAT | 185X | 99.10% | 54.80% | 26% | -
Maximum Reported TDV | 305X | 25X | 54.80% | 26% | 8X
Maximum Reported Power Reduction | - | 10X | - | - | 2X

## Slide 41: Conclusion
It is important to have test compression hardware in commercial chips for reducing TAT and TDV
Test Coverage and Compression are some what inversely proportionate to each other and even with compression requires fullscan top-off patterns
Test coverage can be affected using compression hardware due to data correlation for testing in a TAM architecture
For multicore scan shift interleaving is a good way to reduce peak power

## Slide 42: Discussion questions
Why does a serializer and deserializer over the existing TAM architecture adds more coverage over the existing compression hardware?
Why does SmartScan architecture need less number of fullscan top-off vectors than the conventional compression architecture?
Why is in some case the initial fault coverage is as low as 82% for existing compression scheme?
How to improve coverage and power consumption on top of the SmartScan architecture?
How feasible is to incorporate the idea of scan compression at UVa test chips?

## Slide 43: Papers
[1] Chakravadhanula, K.; Chickermane, V.; Pearl, D.; Garg, A.; Khurana, R.; Mukherjee, S.; Nagaraj, P., "SmartScan - Hierarchical test compression for pin-limited low power designs," Test Conference (ITC), 2013 IEEE International , vol., no., pp.1,9, 6-13 Sept. 2013
[2] Muthyala, S.S.; Touba, N.A., "Improving test compression by retaining non-pivot free variables in sequential linear decompressors," Test Conference (ITC), 2012 IEEE International , vol., no., pp.1,7, 5-8 Nov. 2012
[3] Muthyala, S.S.; Touba, N.A., "SOC test compression scheme using sequential linear decompressors with retained free variables," VLSI Test Symposium (VTS), 2013 IEEE 31st , vol., no., pp.1,6, April 29 2013-May 2 2013
[4] Wohl, P.; Waicukauski, J.A.; Neuveux, F.; Maston, G.A.; Achouri, N.; Colburn, J.E., "Two-level compression through selective reseeding," Test Conference (ITC), 2013 IEEE International , vol., no., pp.1,10, 6-13 Sept. 2013
[5] Bhatia, S., "Low power compression architecture," VLSI Test Symposium (VTS), 2010 28th , vol., no., pp.183,187, 19-22 April 2010